## Slide 1: Titolo presentazione sottotitolo
Milano, XX mese 20XX
Extended project work
A Gazebo car simulator, analysis and comparison with a single-track model

## Slide 2: MIT racecar Model schematic

## Slide 3: URDF standard Links
Inertial parameters: mass, inertial matrix, COG position
Visual parameters: how it is rendered in the simulation
Collision parameters: how to perform collision detection with other bodies
Used to describe a rigid body, can be configured specifying:

## Slide 4: URDF standard Joints
Link type (n of free DOFs): revolute, continuous, prismatic, fixed, …
Parent and child links to be joined
Used to describe connections between rigid bodies and the motions allowed, can be
configured specifying:

## Slide 5: Our System Description

## Slide 6: Topics
[SUB] /virtual_velocities Used to retrieve desired velocities of the reference points computed by trajectory tracker.
[SUB] /vesc/odom Used to retrieve the rotation of the car on the z-axis.
[PUB] /vesc/ackermann_cmd_mux/input/navigation/  Used to publish V and φ (steering angle), which are the results of linearization. These values are read by Gazebo to make the car move. They are put into an AckermannDriveStamped message.

## Slide 7: Change of coordinates applied

## Slide 8: Parameters
L  Distance between front and real axle.
ε  Distance between center of gravity and a point P, along velocity vector. Linearization is done around point P.

## Slide 9: Trajectory Tracker Overview

## Slide 10: Trajectory Tracker Trajectory generator
Computes the next trajectory setpoint given the desired trajectory shape and the time t elapsed since the starting of the motion.
From trajectory_tracker.yaml we can select the desired trajectory shape and the parameters relative to the specific shapes (e.g., speed, direction, sizes, …)

## Slide 11: Trajectory Tracker Reference and output transformations
Since we linearized around fictitious point P (which does not coincide with the car COG), we need two changes of coordinates
before applying the control law.
to adapt the generated trajectory from the COG to P
(P will track the translated trajectory so that the COG
follows the desired path)
to get the coordinates of point P (xP , yP )
given those of the COG (x,y)
Where PL is the distance between point P and the car COG

## Slide 12: Trajectory Tracker Trajectory generator
Linear
The shapes already implemented are:
Parabolic
Circular

## Slide 13: Trajectory Tracker Trajectory generator
8-shaped
Parabolic
Curtate Cycloid

## Slide 14: Trajectory Tracker Controller
Implemented two identical PID controllers with feedforward, one for
each controlled dimention
However, a simple P controller with velocity feedforward is enough
to obtain good results.

## Slide 15: Plugin: gazebo_ros_pacejka
Pacejka Magic Formula
Longitudinal slip
Lateral slip

## Slide 16: Plugin: gazebo_ros_pacejka
Parameter values of the Pacejka Magic Formula

## Slide 17: Plugin: gazebo_ros_pacejka wheel_slip_pacejka
This plugin updates ODE wheel slip parameters (force-dependent slips)
Dynamic friction coefficient

## Slide 18: Plugin: gazebo_ros_pacejka Tests
Eight-shape trajectory

## Slide 19: Plugin: gazebo_ros_pacejka Tests
Linear trajectory

## Slide 20: Tests Gazebo simulator

## Slide 21: Tests ODE single track

## Slide 22: Firma convenzione Politecnico di Milano e Veneranda Fabbrica del Duomo di Milano
Aula Magna – Rettorato
Mercoledì 27 maggio 2015